## Slide 1: Efficient Opportunistic Relay with D2D Communication Techniques
Vincenzo Mancuso, PhD
Research Associate professor
IMDEA Networks Institute
vincenzo.mancuso@imdea.org

## Slide 2: Motivation
Notes: Since the first g we always improved
But never enough to meet user’s demand.

## Slide 3: Efficiency in dense networks
Problem:
  Non-efficient use of cellular spectrum due to interference
  Too much (not real-time) traffic has to be delivered through the cellular network infrastructure
Opportunistic Scheduling
(Unfairness/Complexity)
Clustering
(Static/Dynamic)
Possible solutions:
For selected services, schedule only good users (channel opportunistic scheduling)
Allow all users to exchange contents when they are in radio range (opportunistic relay/clusters)
D2D as enabling technology

## Slide 4: D2D Communications
Legacy
D2D
Definition:
Direct communication between two mobile users without traversing the Base Station or core network (e.g., with WiFi Direct, LTE Direct, LTE-U, Bluetooth, …)

## Slide 5: Channel Opportunistic Scheduling
Resource Blocks
64 QAM
QPSK
Goal:
Using the channel with the highest rate to achieve higher efficiency.
16 QAM

## Slide 6: Clustering
Goal:
Grouping users to leverage cooperative gain.

## Slide 7: Opportunistic D2D communications
Goal:
Relay through the user with better channel quality.
WiFi (D2D) connection
Cellular connection
Cluster Head
Cluster Client
Two-Tier Scheduling

## Slide 8
Theory

## Slide 9
CL(WRR): At each scheduling epoch, resource blocks are divided among cluster heads according to the size of their clusters.
RB1
RB2
Cluster 2
Cluster 1
RB4
RB5
RB6
Frequency
Time
RB3
Low Complexity
Fairness
Inter-Cluster Scheduling Mechanism

## Slide 10
CL(MR): At each scheduling epoch, resource blocks are allocated to the cluster head with the highest channel quality.
Cluster 2
Cluster 1
RB6
RB5
RB4
Frequency
Time
RB3
RB2
RB1
RB6
RB5
RB4
Frequency
Time
RB3
RB2
RB1
Throughput Optimal
Low Complexity
Inter-Cluster Scheduling Mechanism

## Slide 11
Throughput + Fairness
Both CL(MR) and CL(WRR) have comparable throughput gains.
Good
Average
Poor
CL(MR) is unfair when the number of poor users increases.
Jain’s Fairness Index

## Slide 12
Throughput + Energy efficiency
Good
Average
Poor
Throughput gain up to 50%.
Energy efficiency gain up to 30%.

## Slide 13: Cluster Formation & Revenue Distribution
Cluster formation based on Merge & Split[1] : Merge if , otherwise split.
Several methods to share the gain inside cluster:
Equal share allocation
Weighted share allocation
Shapley value
A coalitional game:
[1] W. Saad, Z. Han, M. Debbah, A. Hjorungnes, and T. Basar. Coalitional games for distributed collaborative spectrum sensing in cognitive radio networks. In Proceedings of IEEE INFOCOM, pages 2114–2122, 2009.
Definition of the game:
Join if throughput is improved.

## Slide 14: Intra-Cluster Scheduling
Equal share allocation
10%
30%
60%
Weighted share allocation
Shapley …
Gain? Just Throughput? What about energy, efficiency, etc.?

## Slide 15: Throughput and Power Analysis
Expected achievable throughput under CL(WRR)[2]:
Power consumption of a D2D user over LTE or WiFi[3]:
[3] Arash Asadi and Vincenzo Mancuso , “DRONEE: Dual-radio Opportunistic Net- working for Energy Efficiency”, Elsevier Computer Communications, 2014.
[2] Arash Asadi and Vincenzo Mancuso, “On the compound impact of opportunistic scheduling and D2D communications in cellular networks”, in Proceeding of the ACM MSWIM, Barcelona, Spain, 2013.

## Slide 16: Simulation results (static nodes)
2
4
6
8
Higher Efficiency, although two interfaces are used
86.4%
16.9%
3 Classes of users
RR:
PF:

## Slide 17: Simulation results with mobility
13% Gain
75% Gain
CL(WRR) has better fairness than PF!
Equal Share (ES)  High fairness  low motivation
Weighted Share (WS)  Low fairness  high motivation

## Slide 18
Can D2D further enhance fairness without throughput penalty?
Leverage scheduling ties to adjust fairness
Complete analysis available, we have designed smart stochastic tie-breaking rules
Very high complexity, heuristics needed
Does D2D help? How?

## Slide 19
BeLF
PIKe
The network is mapped to a binary tree. In each recursion, the WRR priority is computed between the two groups based on the maximum of the channel qualities within each group.
Drawback: It does not work well when the branches have very different channel quality.
n(0,0)
{U1, U2, U3}
n(2,1)
{U1}
n(2,0)
{U2}
n(1,1)
{U3}
n(1,0)
{U1, U2}
β(1,1) = 1 - β(1,0)
α3 = β(0,0) . β(1,1)
β(2,0)
α1 = β(0,0) . β(1,0) . β(2,0)
β(2,1)= 1 - β(2,0)
α2 = β(0,0) . β(1,0) . β(2,1)
β(1,0)
β(0,0) = 1
The probability of the tie between each user n and the rest of the users is computed. The throughput hidden in the ties is distributed among users as follows:
If a user receives more than 1/N of the total throughput, it pushes the αn to be negative. We propose the following transformation to preserve positive weights:
Drawback: It is not an optimal approach.
Simple heuristics

## Slide 20
Measurement results I: no clustering
We recorded the SNR of 15 Android phones in our offices

## Slide 21
Using clustering techniques, we increase the ties and therefore the chance of improving fairness
Measurement results II: with five clusters
So, yes, clustering helps by generating ties, and D2D is needed to manage the clusters without missing channel opportunities

## Slide 22
Tie-breaking results

## Slide 23: More applications
Combine ICIC and D2D opportunistic gain
Optimized D2D mode selection
  Inband, outband, …
  WiFi, LTE-U, …
Support for mobile edge computing (MEC)
  Online games
  Virtual, distributed data centers
…

## Slide 24
Protocol

## Slide 25: Integration into LTE-A and WiFi Direct[4]
Cluster formation over WiFi Direct
Cluster registration
Bearer establishment
Mobility
Data plane operations
LTE procedure adaptation
[5] Arash Asadi and Vincenzo Mancuso, “WiFi Direct and LTE D2D in Action”, in Proceeding of the IEEE Wireless Days, Valencia, Spain, 2013.

## Slide 26: Data Flow from UE to eNB
Qi+1
Qi
Qi-1
TCP/UDP
IP
LTE PDCP
Cluster client i
Cluster head
WiFi Channel
Cluster clients’ traffic
TCP/UDP
IP
LTE PDCP
RLC
MAC
PHY
MAC
PHY
Local traffic
PDCP
RLC
MAC
PHY
LTE Channel
PDCP PDUs
PDCP PDUs
MAC
PHY
…
…
Qi-1
Qi
Qi-1
Scheduler
…
…
…
…
Transparent Tunnel
PDCP to RLC tunneling for higher security and performance.
Platform integration with minor modifications.

## Slide 27
Experiment

## Slide 28: Prototyping the First SDR-based D2D Testbed[5]
[5] Arash Asadi, Vincenzo Mancuso, and Rohit Gupta, “An SDR-based Experimental Study of Outband D2D Communications”, Accepted in IEEE INFOCOM, San Francisco, USA, 2016.

## Slide 29: Hardware Components
Convolutional
coding
Interleaving
Scrambling
Bit to IQ Symbol mapping
MUX
PSS
Reference Sym
Null
iFFT & Resampling
DAC
FPGA
FAM
Mac
Services
Transport Block
Generation
D2D
Services
CCH
SCH
Resource
Mapping
Real-Time Controller
PXIe 8135
(Real-Time controller)
FlexRIO module
(RF transceiver)

## Slide 30: SDR Software

## Slide 31: Experimental Results
Schedulers:
    Round Robin (RR)
    Proportional Fair (PF)
    Clustered RR (CL(RR))
    Clustered PF (CL(PF))
LTE (RX)
WiFi
LTE (TX)
Less than 3 ms
11%
21%

## Slide 32: Experimental Results
Notes: Structural similarity (SSIM). QoE metric based on the difference with the original

## Slide 33: Experimental Results
CSI
CSI
CSI
71.8%

## Slide 34: Conclusion
Opportunistic D2D communications feeds on Density.
Analytical and experimental results illustrated higher efficiency.
Leveraging new paradigms and existing tools.
Densification
Complexity
Spectrum Scarcity
Simulation
Theory
Experiment
Feasibility of Opportunistic D2D Communications

## Slide 35: Future Works
Dense Scenarios

## Slide 36: Future Works
Public Safety

## Slide 37
and many thanks to Arash Asadi, PhD, who successfully defended in March with this work and a similar presentation